import numpy as np
from uncertainties import unumpy as unp
from uncertainties import ufloat

filename = "Slit"
f = np.loadtxt(f"{filename}.csv", delimiter = ",", skiprows = 1)

# D measured with normal ruler
D = unp.uarray(f[:,0], 1) # Distance from slit to screen (cm)

m = f[:,1] # Order of dark fringe

# Inner and Outer distances between borders of dark fringes
# measured with Vernier Callipers
Outer = unp.uarray(f[:,2], 0.002) # Distance between outer lines (cm)
Inner = unp.uarray(f[:,3], 0.002) # Distance between inner lines (cm)

given_lambda = 650 # nm
given_slit_b = 0.2 # mm

xm = (Inner + Outer)/2

if (filename == "Wire"): # Calculate Wire Thickness b
    wire_b = (2*m*given_lambda*1e-9*D*1e3)/xm # mm
    object = wire_b
else: # Calculate Laser Wavelength Lambda
    calculated_lambda = (given_slit_b*1e-3*xm*1e9)/(2*D*m)	# nm
    object = calculated_lambda

for i in range(len(object)): # Print all values
    print("{:.2uP}".format(object[i]))

print("Average = {:.2uP}".format(np.mean(object)))